## Slide 1
FLORIDADAMP · REED LANG · HUMIDITY
Right-size the AC.
Let it wring the air.
Florida humidity is a time problem. An oversized unit hits setpoint before the coil pulls water out of the air.
Measure first. Size for Florida relative humidity (RH). Drain continuously.

## Slide 2
01 — THE TRICK
02 / 08
COOL IS NOT DRY
68°F can still feel like a swamp.
Temperature
The thermostat won.
An oversized unit dumps enough cold air to satisfy the setpoint in a few minutes. The room is cold. Nobody wants the sofa.
Moisture
The coil lost.
Water condenses only while the coil stays cold and wet. Short cycles leave the grains in the room. That is 60%+ relative humidity (RH) at a “comfortable” setpoint.

## Slide 3
02 — TWO LOADS
03 / 08
SENSIBLE VS LATENT
The same machine does two jobs.
Sensible — temperature
Most of a short cycle is spent dropping °F
Latent — moisture
Needs time on the coil
Florida latent load is a big slice of the job — often a quarter to a third of the cooling load. Square-foot rules of thumb from drier climates skip that. The coil has to run long enough for water to bead, drip, and leave through the drain.

## Slide 4
03 — RUNTIME
04 / 08
SHORT CYCLE
Bigger is not drier.
Oversized
5–8 minutes
Off before the coil is a wet sponge. Thermostat happy. Hygrometer not.
Right-sized
15–20 minutes
Longer run. Coil stays in the condensing window. Water leaves the house instead of the sofa.

## Slide 5
04 — AT HOME
05 / 08
HOW YOU TELL
You can see this without a load calc.
1
Hygrometer on an interior wall
Away from the supply vent and the slider. Target about 45–55% relative humidity (RH). Sustained above 60% is the action cue.
2
Watch one cooling cycle
If it hits setpoint and shuts off in under 10 minutes on a typical afternoon, the unit is likely oversized for that day.
3
Do not use the thermostat as a meter
Dropping to 68°F is not dehumidification. Fan ON re-evaporates a wet coil into the house. AUTO.

## Slide 6
05 — SIZING
06 / 08
MANUAL J
Ask for Manual J. Skip the square-foot banner.
Manual J
A room-by-room load. Windows, insulation, orientation, infiltration. Florida latent load is in the number.
Manual S
Picks the machine that matches that load. Total tons is not the same as latent capacity.
Fan AUTO
Fan ON after a cycle blows wet-coil air back into the rooms. AUTO lets the coil drain.
Data plate
Read tons vs square feet as a first check. Then log relative humidity (RH). A contractor finishes the calc.

## Slide 7
06 — BACKSTOP
07 / 08
WHEN AC LOSES
Right-size first. Then backstop the grains.
Mild rainy days, shoulder season, and empty houses: the compressor barely runs. No runtime, no wringing. A dedicated dehumidifier keeps working on a humidistat, drained continuously — not a bucket.
Do not
Do not size the next AC from a square-foot banner.
Do not drop the thermostat to 68°F and call it humidity control.
Do not run the fan ON all day.
Do not skip the hygrometer.

## Slide 8
07 — RUN THIS
08 / 08
FLORIDADAMP
Three checks this week.
01
Log relative humidity (RH)
Interior wall, morning and late afternoon, seven days, normal setpoint 74–76°F.
02
Time a cooling cycle
If it is off in under 10 minutes while the hygrometer sits above 60%, the machine is cooling faster than it dries.
03
Then size the backstop
Keep AUTO. Ask for Manual J on the next changeout. See floridadamp.com/fl-dehumidifier/measure/